## Slide 1
Online EEG + NIRS hand imagery
Three-class classifier for the competition
Public subject holdout evaluation | September 2026
Notes: Seven-minute competition presentation. Results come from the supplied public competition sessions and the frozen local scorer.

## Slide 2
Task and online contract
Predict rest, imagined left hand, or imagined right hand.
A one-second EEG window arrives every 250 ms; NIRS may be absent.
Block 1 trains the model. Later labels arrive only after each block.
The scorer averages each session's worst-class F1 and macro recall.
Notes: Source: supplied competition specification, sections 3 and 5.

## Slide 3
Signal processing and model
Causal 1-40 Hz filter with persistent IIR state.
EEG band power plus C3/C4 asymmetry; HbO/HbR window statistics.
Three Random Forests: EEG, NIRS, and combined features.
After every finished block, fit using released labels and past-session features.
Notes: Source: included classifier.py and report/METHODS_EN.md.

## Slide 4
Validation split
56 public sessions across 14 people.
Model selection: N15/N16 held out; 38 compatible other sessions train the cache.
Final check: N17/N18 held out; 46 compatible other sessions train the cache.
The eight test sessions come from two people, not eight independent people.
Notes: Source: included training manifests, public_data_manifest.csv, and eight held-out metric files.

## Slide 5
Independent N17/N18 results
Hard agreement
Probability fusion
63.67% accuracy
65.18% accuracy
0.4050 worst-class F1
0.4152 worst-class F1
50.2353 / 130 points
51.2448 / 130 points
Measured before the speed refactor; jury design points excluded.
Notes: Source: results/holdout/baseline_N17_N18 and final_selected_N17_N18, frozen score.py.

## Slide 6
Where the gain comes from
The measured decision change was probability fusion:
50% combined model + 35% EEG model + 15% NIRS model.
Six of eight sessions gained score; two lost score.
Mean gain: 1.01 points. Illustrative bootstrap interval: -0.58 to +2.52.
Notes: Source: included paired per-session metrics and 20,000 seeded session-level bootstrap resamples.

## Slide 7
Submission and limits
Final cache: 54 usable public recordings, intended for hidden sessions.
Frozen judge runner and scorer stay unchanged.
Windows smoke test and an eight-session strict replay are included.
Full 56-session replay, hidden results, and platform timing are pending.
Notes: Source: solution/artifacts training manifest, DEPLOY.md, and included validation outputs.